## Slide 1: Intermediate Presentation
SVBRDF Estimation using a Physically-based Differentiable Renderer Markus Andreas Worchel

## Slide 2: Recap – Topic
Physically-based
Differentiable Renderer
CNN
…
…
…
…
…

## Slide 3: Recap – Schedule
Download database
Acquire testing and training code for the network
Get familiar with papers, source code and data
Acquire code for Mitsuba 2
Replace rendering layers of the network with Mitsuba 2
Evaluation (compare with unmodified method)

## Slide 4: Data
Single-view database (87 GB)
  Input image and material variations generated offline
  Reading implemented ✓
Multi-view database (1.4 GB)
  Input images and material variations generated at load time
  Reading (generation) not yet implemented –

## Slide 5: Models
Single-view Model (Deschaintre et al., 2018)
  Implement in pyTorch ✓
  Verify model using visualization in TensorBoard ✓
  Report bugs back to author ✓
Multi-view Model (Deschaintre et al., 2019)
  Implement in pyTorch ✓ → Only 40 LoC more than single-view model
  Verify model using visualization in TensorBoard –

## Slide 6: Training Loss
?
Prediction
Ground Truth
Model
…
…
…

## Slide 7: Loss – From L1 to Mixed Loss
L1 loss between SVBRDF maps was implemented last time
Now: Mixed Loss
Rendering operator requires a differentiable renderer and scene(s)

## Slide 8: Loss – Renderer
Implement simple differentiable renderer ✓
  Only considers direct illumination
  Lambertian diffuse term
  Cook-Torrance specular model
  Renders SVBRDF on flat material patch in the origin (virtual orthographic camera)
💡
📷
Perspective
Orthographic

## Slide 9: Loss – Scenes
One camera, one light ✓
Randomly sampled camera and light positions per mini batch –
  Required for unbiased appearance comparison
  Currently only three fixed configurations:
Multiple Lights –

## Slide 10: Loss – Results
Input
Ground Truth
L1 Loss
Mixed Loss (L1 + Rendering)

## Slide 11: Replacing the Simple Renderer
Mitsuba 2 still not released
  Fall back to Redner ✓
Redner is not compatible with Windows
  Patch Redner code (MSVC intrinsics, install script) ✓
  Send PR to upstream repository ✓
Uses OpenEXR python bindings (no Windows compatibility)
  Patch OpenEXRPython code ✓
  Send PR to upstream repository ✓
Redner GPU (CUDA) not compatible with Windows
  Patch Redner Code –
  Send PR to upstream repository –

## Slide 12: Replacing the Simple Renderer
Integration into rendering loss and current structure –
  Redner scene definition vs. my scene definition
  Orthographic rendering
Training time feasibility check –
  Path tracing is resource and time demanding
  GPU implementation is probably a must
Evaluation –
  Full training of models
  Qualitative (and quantitative) comparison
  Training time comparison

## Slide 13: Conclusion
Training data generation to be done
Single-view and multi-view models are implemented
Simple renderer is implemented
Mixed loss (L1 + rendering loss) partially implemented
  Random sampling of scene parameters to be done
Redner CPU ready to use with Win32
  Integration into rendering loss to be done
  GPU compatibility to be done
Evaluation of model trained with Redner to be done
→ Most difficult tasks are finished or basis is established